SECTION 01 5705

TEMPORARY CONTROLS AND COMPLIANCE REQUIREMENTS

*************************************************************************************************************

LANL MASTER SPECIFICATION

When editing to suit project, author shall add job-specific requirements and delete only those portions that in no way apply to the activity (e.g., a component that does not apply).  To seek a variance from applicable requirements, contact the ESM Civil POC.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General Requirements.

Delete information within “stars” during editing.

Specification developed for ML-3 / ML-4 projects.  For ML-1 / ML-2, additional requirements and QA reviews are required.

*************************************************************************************************************

PART 1 	GENERAL

SECTION INCLUDES

Erosion and Sediment Control

Storm Water Management

Site Stabilization

Spill Control and Response

Debris Control

Air Quality

Dust Suppression

Rodent Control

Environmental Restoration Sites

Hazardous Waste

Traffic Control

Water Discharge

Grading, Excavating and Trenching

Concrete Washout, Potholing, Directional Drilling

SUBMITTALS

Submit the following in accordance with Section 01 3300, Submittal Procedures.

For projects operating under a National Pollutant Discharge Elimination System (NPDES) permit:

Submit all requested information for the Storm Water Pollution Prevention (SWPP) plan within 14 days after award of the contract. Submit information in sufficient format and detail as may be required by LANL for completion of the SWPP Plan, including the calculations required by the New Mexico Environmental Department (NMED) Surface Water Quality Bureau (SWQB) state certification of the proposed NPDES permit NMR 150000 sections 9.c.1.a.i and 9.c.1.b: http://www.nmenv.state.nm.us/swqb/PSRS/NMR150000-Info.html  The completed SWPPP Plan shall be certified by both LANL and a responsible corporate officer of the Contractor prior to the Notice of Intent (NOI) submittal.  The Contractor agrees to continue to submit such additional information to and otherwise cooperate and work with LANL to maintain/modify the SWPP Plan throughout the duration of this contract.

Construction shall not begin until at least 7 days after the United States Environmental Protection Agency (EPA) has acknowledged receipt of the complete NOI on their website at http://www.epa.gov/npdes/stormwater/cgp and the (EPA) has not delayed the authorization. The Contractor shall submit a complete Notice of Intent (NOI) for review to LANL at least 20 days prior to start of construction.  The SWPP Plan shall be completed and approved prior to submission of the NOI.  Once LANL has reviewed and approved the NOI, the Contractor shall submit the NOI to the EPA at least 8 days prior to start of construction.

Following a review and approval by LANL, submit a Notice of Termination (NOT) to the EPA within 10 days after final stabilization of the site.  Release of the site before final stabilization may be negotiated through LANL prior to termination of the contract.

New Mexico Environment Department Notice of Intent (NMED NOI)

The LANL Construction Inspector will contact the LANL Water Quality & Hydrology Group (ENV-RCRA) at 665-0453 prior to the Contractor using fertilizer, hydraulically applied mulches, Bonded Fiber Matrix, dust suppression additives, and other substances that are applied to the ground. ENV-RCRA will determine whether the substances will require a Notice of Intent (NOI) to Discharge be submitted to the New Mexico Environment Department (NMED) by Contractor. Provide information as necessary to obtain the NMED NOI and follow all conditions of the NOI.

Traffic Control Plan

Submit a temporary traffic control plan and subsequent proposed changes to the plan to the LANL Traffic Control Engineer for review and approval.

PRODUCTS

Not Used

EXECUTION

  - Erosion and Sediment Control

Properly install Best Management Practices (BMPs) as shown on the drawings or identified in the SWPP Plan, prior to any earth disturbing activity.

Maintain BMPs in accordance with SWPP Plan and manufacturer’s recommendations.

When practical, implement permanent BMPs during the construction phase to meet the objectives of temporary sediment and erosion controls.

Disturb only the minimum amount of soil necessary.  Give special attention to protecting established vegetation.

Storm Water Management

*****************************************************************************************

Refer to the Civil Chapter, G10 Site Preparation, for Storm Water Management design requirements.

*****************************************************************************************

Provide methods to control surface water as identified in the Drawings or SWPP Plan to prevent damage to the Project, the site, and in adjoining areas.

Use permanent storm water management controls (such as detention ponds, riprap, rock check dams, etc.) during the construction in place of temporary storm water management controls whenever practical.

Ensure temporary and permanent storm water management controls are properly installed per Drawings and the SWPP Plan.  Maintain controls per Drawings, the SWPP Plan, and manufacturer’s installation recommendations.

site stabilization

Stabilize all disturbed areas with native perennial vegetation, gravel, riprap, pavement, buildings, or other permanent stabilization measures.  Do not leave any disturbed areas as barren soil.  Final stabilization shall be accepted by LANL Utilities and ENV-RCRA.   The LANL Construction Inspector will contact LANL Utilities at 665-0106 and ENV-RCRA at 665-0453 to schedule the final walk down and acceptance.

For seeded areas, establish an evenly distributed native perennial vegetative cover with no large bare areas and an average density of 70% of the native background vegetative cover for the area.  Refer to Section 02936, Seeding.

Begin stabilizing disturbed areas no more than 14 days after construction activities have finally or temporarily ended in the area.

Do not apply fertilizer, hydraulically applied mulches, or Bonded Fiber Matrix in watercourses.

Spill control and response

In the event of a spill, immediately notify the LANL Construction Inspector who will contact Emergency Management and Response (EM&R) at 667-6211.  The Contractor shall be responsible for remediation of any spill.

Store all fuels, lubricants, chemical storage, material stockpiles, and other potential pollutants in a designated area on-site.  Provide secondary containment and controls including berming lined with an impervious material, covering, or other appropriate BMPs. When aboveground petroleum storage capacity is greater than 1,320 gallons (including all containers 55 gallons or larger), notify the LANL Construction Inspector who will contact ENV-RCRA at 665-0453 to initiate the development of a Spill Prevention Control and Countermeasure (SPCC) Plan.

When an aboveground petroleum storage tank (AST) is being constructed with a storage capacity greater than 1,320 gallons and less than 55,000 gallons, submit information in sufficient format and detail as required by LANL for completion of the Corrosion Prevention Plan (CPP), the tank registration, and state notification.  The CPP must be certified by a corrosion expert or a PE and approved in writing by New Mexico Environment Department – Petroleum Storage Tank Bureau (NMED-PTSB) prior to installation of the tank system.  The AST system must be registered with NMED-PTSB prior to being placed in service.  Personnel who are certified by the NMED-PTSB shall install all AST systems.

The LANL Construction Inspector will contact ENV-RCRA (665-0453) at least 60 days prior to performing repairs or modifications to existing AST systems.  If the repair or modification is an emergency repair, notify ENV-RCRA as soon as possible following the repair.  Personnel who are certified by the NMED-PTSB shall perform all modifications or repairs to AST systems.

The LANL Construction Inspector will contact ENV-RCRA (665-0453) at least 60 days prior to installing any underground petroleum storage tanks to ensure that all LANL requirements are met.

Debris Control & Soils management

Use good housekeeping practices to keep sites free of construction debris and trash.  Provide containers for deposit of debris and trash.

Do not drive or move any vehicle on any public road unless the vehicle is constructed, loaded, secured or covered in a manner that will prevent any of its load from dropping, sifting, leaking, or otherwise escaping (except when purposefully cleaning, maintaining, or sanding for traction).

Securely fasten all load covers to vehicles prior to driving on public roads so that the covering does not come loose or become a hazard to others.

Do not bury construction waste, sanitary waste, or trash on-site.

Do not move soil or other material between Technical Areas (TAs) without first obtaining written approval from the receiving TA.  Material must be clean of all contaminates before movement; all transferred soil must be characterized.  See Part 3.9C.

Segregate all materials prior to sending material to the LANL Material Recycle Facility (MRF).  The LANL Construction Inspector will contact LANL Solid Waste Regulatory Compliance (ENV-RCRA) at 667-0666 to obtain instruction on required sampling and documentation procedures.  Material shall be clean of all contaminates.

Air quality

The LANL Construction Inspector will contact the ENV-EAQ Group (665-8855) prior to the Contractor operating portable and stationary fuel burning equipment (e.g., generators, rock crushers, asphalt plants).  Drivable equipment does not require notification of ENV-EAQ.

The LANL Construction Inspector will contact ENV-EAQ Group Office (665-8855) if the Contractor stores over 500 pounds of chemicals at the site.

Dust suppression

When applying potable water for dust control, ensure compliance with Section 01 3545, Water Discharge Requirements.

Do not add additives to potable water for dust control until receiving approval.  Notify the LANL Construction Inspector who will contact ENV-RCRA.  Comply with all conditions specified by ENV-RCRA and the applicable federal and state agencies.  Apply all liquids in a manner that does not result in runoff.

Do not apply dust suppression additives or other substances in watercourses.

Rodent Control

Do not use any pesticide (rodenticide) without the written approval of LANL.  Comply with New Mexico Pesticide Control Act, Chapter 76, Article 4, Sections 1-39.

environmental restoration site

******************************************************************************

Refer to the Civil Chapter, Section G10 Site Preparation, for environmental restoration design requirements.

*******************************************************************************

No storm water runoff or soil disturbance shall be allowed across a Potential Release Site (PRS), includes Solid Waste Management Units (SWMUs) and Areas of Concern (AOCs) that are identified in the contract documents.

A PRS cannot be disturbed without LANL Remediation Services (ERSS-RS) Project approval and oversight.  The LANL Construction Inspector will contact ERSS-RS at 665-5138 or 665-2198.  Any worker conducting work within the boundary of a PRS must be made aware, by the LANL Project Manager, of the potential contaminants present in soils and other materials at the site and the potential hazards associated with those contaminants.

Any soil or other material removed from a PRS boundary and not returned to the point of excavation must be managed, characterized, and disposed of by the Contractor in accordance with all applicable LANL waste management requirements including approved Waste Profile forms, waste accumulation areas, etc., or if the project causes additional runoff to cross the site, install appropriate sediment & erosion controls prior to construction activities.  Best Management Practices (BMPs) for the Storm Water Pollution Prevention (SWPP) Plan and/or soil erosion control must be in place for all projects prior to the start of any soil disturbing activities within a PRS to prevent potential contaminant migration.

Hazardous and mixed Waste

Store, treat, and/or dispose of hazardous or mixed wastes in accordance with applicable laws and regulations, and LANL requirements.

Register satellite accumulation areas or less than 90 days storage areas with LANL ENV-RCRA Group prior to storing, handling, treating, or disposing of hazardous or mixed waste.

Contact the ENV-RCRA Group (667-0666) for more information on the management of hazardous or mixed waste, New Mexico special waste (such as petroleum contaminated soil, spills, chemical products, asbestos waste, infectious waste, etc.), PCBs, construction and demolition debris, and other types of solid waste.

Traffic control

****************************************************************************

Refer to the Civil Chapter, Section G2010 Roadways, for traffic consideration design requirements.

*****************************************************************************

A temporary traffic control plan shall be prepared by a registered Professional Engineer (PE) who is certified as a Professional Traffic Operations Engineer (PTOE).  The detail shall be appropriate to the complexity of the work project and submit to the LANL Traffic Control Engineer for review and approval.  The LANL Traffic Control Engineer shall approve any proposed changes in the temporary traffic control plan.

The temporary traffic control plan shall start in the planning phase and continue through the design, construction, and restoration phases.  The temporary traffic control plans and devices shall follow the principles set forth in the MUTCD, latest addition.  Temporary traffic control plans may deviate from the typical applications described in the MUTCD based upon engineering judgment, to allow for conditions and requirements of a particular site.

Consider and address the safety of pedestrians in the Traffic Control Plan, and if altering pedestrian traffic, provide an alternate pedestrian route.

Traffic control devices shall be properly maintained during the project.

Water discharge

Follow Section 01 3545, Water Discharge requirements.

Grading, excavating, and trenching

Follow Section 31 2000, for Earth Moving requirements.

3.14  	Concrete Washout, Potholing, Directional Drilling

A.  	Washout of concrete waste will be performed within a defined area surrounded by a Triangular Silt DikeTM, compacted earth berm, or other appropriate control that acts as a continuous line barrier to prevent the runoff of washout material and the co-mingling of unset concrete with storm water or entry into a watercourse. Properly dispose of all hardened excess concrete following evaporation or infiltration of all liquid from the concrete waste confined within the defined area.

B.  	Liquids from potholing activities must be placed within a defined area within the project site limits surrounded by a Triangular Silt DikeTM, compacted earth berm, or other appropriate control, until the liquids evaporate. Properly dispose of solids. Contact the LANL Water Quality Group prior to performing any potholing activities to ensure an NOI is submitted to New Mexico Environment Department (NMED). Do not discharge polypropylene glycol, propylene glycol, ethylene glycol, or any other anti-freeze substance without contacting LANL to ensure all environmental requirements have been met. Potholing material may not be removed from the site; refer to Part 3.5E.  (Check this Part number if renumbering, F. to E.)

C.  	Directional Drilling mud must be placed within a lined retention pond until the liquids evaporate or immediately properly disposed of. Properly dispose of solids. Mud from drilling operations involving a SWMU or PRS must first be evaluated for contaminates before disposal occurs.  Contact the LANL Water Quality Group at 665-0453 and the LANL RCRA Group at 667-0666 for additional guidance.

END OF SECTION

*********************************************************

Do not delete the following reference information:

*********************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 01 5705, Rev. 1, dated November 28, 2006.