SECTION 05 5350

METAL GRATINGS AND FLOOR PLATES

*************************************************************************************************************

LANL MASTER SPECIFICATION

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project -- and specifier’s notes such as these.  To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual Structural Specifications POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Ch 1 Section Z10 Specifications and Quality sections.

Note:  Aluminum has no known national standard for nuclear design analogous to AISC N690 so it is generally not suitable for PC-3 and PC-4 structures.
*************************************************************************************************************

PART 1  GENERAL

1.1	SECTION INCLUDES

- Formed steel gratings.

B.	Formed aluminum gratings.

C.	Molded glass fiber gratings.

D.	Fabricated steel floor plates.

1.2	DESIGN REQUIREMENTS

A.	Use NAAMM A202.1 for design loads.

B.	Design for live load of [100 psf].

C.	Maximum deflection under live load is 1/240 of span.

1.3	SUBMITTALS

A.	Submit the following in accordance with Section 01 3300, Submittal Procedures:

1.	Catalog data with details of grate construction, and span and deflection tables.

PART 2  PRODUCTS

2.1	GRATING MATERIALS

A.	[Use formed and galvanized steel conforming to ASTM A36, G90.]

B.	[Use formed aluminum conforming to ASTM B221, Alloy 6063-T6.]

*************************************************************************************************************

If glass fiber grating will be exposed to harsh chemicals, select the plastic binder to resist them.

*************************************************************************************************************

C.	Use molded glass fiber reinforced plastic conforming to [            ].

D.	Provide appropriate anchorage and splicing fittings.

2.2	FLOOR PLATE MATERIALS

A.	Use diamond plate galvanized steel sheet conforming to ASTM A526, G90.

2.3	GRATING FABRICATION

A.	Fabricate grating to accommodate design loads.

B.	Mechanically clinch joints of intersecting metal grating sections.

C.	Provide non-slip top surface.

2.4	FLOOR PLATE FABRICATION

A.	Shear steel plate to size required, and grind edges to provide an ”eased” edge.

B.	Galvanize after cutting and grinding.

PART 3  EXECUTION

3.1	INSPECTION

A.	Verify that opening sizes and dimensional variations are acceptable to receive grating [floor plates].

B.	Verify that supports are correctly positioned.

3.2	INSTALLATION

A.	Install components in correct position, plumb and level.

B.	Secure to prevent movement with appropriate fittings.

END OF SECTION

**********************************************************

Do not delete the following reference information:

**********************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 05 5350 Rev. 1, dated May 1, 2008.