SECTION 07 0150.19

PREPARATION FOR RE-ROOFING

*************************************************************************************************************

LANL MASTER SPECIFICATION

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project -- and specifier’s notes such as these.  To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1 Section Z10 Specifications and Quality sections.
*************************************************************************************************************

GENERAL

SECTION INCLUDES

[Removal] [Partial removal] [Scarification of surface] of existing roofing system in preparation for new roof membrane system.

UNIT PRICE - MEASUREMENT AND PAYMENT

New Insulation:

Basis of Measurement:  By the square foot.

Basis of Cost:  Includes complete removal of existing insulation, replace with new insulation of specified thickness and in compliance with Section 07 2113, Board Insulation.

Existing Insulation - Partial Removal:

Basis of Measurement:  By the square foot.

Basis of Payment:  Includes removal of existing insulation, replace with new insulation of specified thickness and in compliance with Section 07 2113, Board Insulation.

Repair Existing [Wood] [Metal] Deck:

Basis of Measurement:  By the square foot.

Basis of Payment:  Includes replacing corroded or rotted or substandard decking with new material of appropriate thickness and type.

SYSTEM DESCRIPTION

*************************************************************************************************************

Use this article carefully; restrict statements to describe components used to assemble system. Do not repeat statements made in SUMMARY Article; “Section includes” paragraph.

Edit the following paragraph to identify principle tasks required for the Project. When more than one area is involved with differing degrees of material removal, generalize the following paragraph and describe areas and extent of work in SCHEDULE at end of this section.

*************************************************************************************************************

[Entire Roof Area:] [Roof Areas as Indicated:][                        :] Remove existing [roofing gravel,] [perimeter flashings,] [base flashings,] [counter flashings,] [vent stack flashings,] [roofing membrane,] [insulation,] [vapor retarder,] [air barrier,] [sheathing,] [damaged deck,] [and] [                              ].

Remove existing lightning protection system and reinstall with new material in accordance with Section 26 4100 or 26 4115 as appropriate.  Return existing air terminals to LANL.

LANL will remove roof mounted [mechanical equipment,] [electrical equipment,] [and] [                    ].  Subcontractor shall allow LANL a minimum of [2] working days notice to accomplish the aforementioned tasks.

COMPLIANCE ISSUES

Roof Membrane Manufacturer’s Requirement.

SUBMITTALS

Submit the following in accordance with Section 01 3000, Submittals:

Field Reports:  Indicate concurrence of thermographic analysis of existing membrane, insulation, and deck.

QUALITY ASSURANCE

International Building Code

PRE-INSTALLATION MEETINGS

Convene minimum one week prior to commencing work of this section.

ENVIRONMENTAL REQUIREments

Do not remove existing roofing membrane when weather conditions threaten integrity of building contents or intended continued occupancy.

Removal of coal tar roof material requires additional personnel protection equipment (PPE) and occupant protection due to the potential of coal tar dust becoming acidic.

Subcontractor personnel will not be exposed to occupant operations hazards while roofing activities are in progress.

SCHEDULING

Schedule Work with building occupants so as not disrupt operations.

Schedule Work to coincide with installation of new roofing or overlay system.

PRODUCTS

  - COMPONENTS

Temporary Protection: Sheet [polyethylene] [fiber reinforced plastic]; furnish sandbag weights to retain sheeting in position.

Protection Board:  When required shall be in conformance with Section 07 2113, Board Insulation.

EXECUTION

  - EXAMINATION

Verify existing roof surface is clear and ready for work of this section and in compliance with roofing manufacturer’s requirements.

PREPARATION

Sweep roof surface clean of loose matter.

Remove loose refuses and dispose off site.

LANL Subcontract Technical Representative (STR) will inspect completeness of preparation.

EXISTING CONSTRUCTION

DEMOLITION

Remove existing roof membrane and loose bituminous materials.

Comply with insulation and membrane manufacturer's instructions for preparation of substrate to receive roofing system.

Clean substrate of dust, debris, and other substances detrimental to the system work.  Remove sharp projections.

Remove metal counter flashings.

For overlay roofs over asphalt or coal tar built up roofs, remove the surface of existing roof material to top most layer of felt. Surface shall be clear of high spots or lumpy areas.

Notify LANL STR to inspect substrate after preparation.  Subcontractor shall not proceed with installation until LANL STR has approved substrate.

Remove metal counter flashings.

*************************************************************************************************************

Paragraph “C” applies when roof is to be overlaid.

*************************************************************************************************************

Scrape or scarify roofing gravel from membrane surface [without causing serious damage to membrane felts].

Remove [damaged portions of] roofing membrane, perimeter base flashings, flashings around roof protrusions, [pitch pans and pockets,] [insulation vents,] [and] [              ].

*************************************************************************************************************

Paragraphs “E” and “F” apply when roof is to be replaced.

*************************************************************************************************************

Remove and replace all damaged portions of roofing [insulation] and [decking].

Remove perimeter base flashings, flashings around roof protrusions, [pitch pans and pockets,] [insulation vents,] [and] [                       ].

*************************************************************************************************************

Paragraph “G” applies when roof is to be overlaid.

*************************************************************************************************************

Cut and lay flat membrane blisters.

Remove [damaged] insulation [and fasteners,] cant strips, blocking, and [               ].

Remove [vapor retarder,] [sheathing paper,] [underlay,] [sheathing,] [and] [          ].

Remove damaged deck materials.

Repair existing [wood] [steel] [concrete] [                     ] deck surface to provide smooth working surface for new roof system.

FIELD QUALITY CONTROL

*************************************************************************************************************

Include this article only when independent inspection or testing will be part of materials preparation and removal process or when exact condition of existing roof system in uncertain. Include additional paragraphs as appropriate.

*************************************************************************************************************

The LANL STR, in coordination with the Subcontractor, will identify [exact] [approximate] limits to material removal as well as field demolition identified areas.

PROTECTION OF INSTALLED CONSTRUCTION

Install temporary protection board over uncovered deck surfaces where materials or walkways are to be determined.

Install temporary sheeting up and over parapets and curbing.  Retain sheeting in position with [weights].  [Temporary fasteners.]

Provide for surface drainage from sheeting to existing drainage facilities.

Do not permit traffic over unprotected or repaired deck surface.

SCHEDULES

*************************************************************************************************************

Include schedule when differing locations require definition as to extent of removal work and identify subsequent roofing system to be installed.

Consider the following examples when developing Project schedule.

*************************************************************************************************************

Main Roof:  Remove flashings, gravel, membrane and underlayment, in preparation for new protected membrane roof system.

Penthouse Roof:  Remove flashings and gravel; provide protection board over existing insulation in preparation for new conventional membrane roof system specified.

END OF SECTION

*****************************************************************

Do not delete the following reference information:

*****************************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 07 0150.19 Rev. 1, dated May 5, 2008.