SECTION 07 0155

ROOF PATCHING

*************************************************************************************************************

LANL MASTER SPECIFICATION

When editing to suit project, author shall add job-specific requirements and delete only those portions that in no way apply to the activity (e.g., a component that does not apply).  To seek a variance from applicable requirements, contact the ESM Architectural POC.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General Requirements.

Delete information within “stars” during editing.

Specification developed for ML-3 projects.  For ML-1 / ML-2, additional requirements and QA reviews are required.

*************************************************************************************************************

PART 1 GENERAL

1.1	SECTION INCLUDES

A.	[Reworking existing roofing at area of penetration installation.]

1.2	SUBMITTALS

A.	Submit the following in accordance with the requirements of Section 01 3000, Submittal Procedures:

1.	Installation instructions for proposed materials.

1.3	QUALITY ASSURANCE

Use a roofing installer that has successfully performed at least 5 projects of similar type and scope.

1.4	ENVIRONMENTAL REQUIREMENTS

A.	Do not remove existing roofing membrane when weather conditions threaten damage to the building, its contents, or the intended continued occupancy of the building.

B.	Maintain weather protection of roof and enclosed spaces below during removal and patching operations.

PART 2 PRODUCTS

2.1	MATERIALS

A.	Single-ply roofing membrane flashing:  Hypalon, 40 mil. thick.

B.	Elastomer mastic:  Tremco "Polyroof".

C.	Reinforcing mesh:  Tremco "BURmesh".

D.	Cant strip:  4in. fiber cant.

E.	Metal Flashing:  26 gauge galvanized sheet metal.

F.	Resaturant:  Tremco "Ecolastic".

PART 3 EXECUTION

3.1	MATERIALS REMOVAL

A.	Remove existing roofing materials within area of [penetration].

B.	[Remove loose aggregate within 10 feet of roof penetration.]

3.2	RE-ROOF OPERATIONS

A.	For curb installations, set cant strip around curb perimeter in bed of mastic.

B.	For curb installations, install upper edge of roofing membrane under sheet metal flashing at top of curb and extending out onto existing roofing.

C.	Seal joint between patch roofing membrane and existing roofing with 5 courses of mastic and mesh.

D.	[Apply resaturant to existing roofing where loose gravel is removed.]

E.	[Rebroadcast gravel over resaturated area.]

end of section

*************************************************************************

Do not delete the following reference information:

*************************************************************************

for lanl use only

This project specification is based on LANL Master Specification 07 0155 Rev. 0, dated January 6, 2006.