SECTION 07 5213.13

atatic-polypropylene modified-bitumen roofing, cold-applied

************************************************************************************************************

LANL MASTER SPECIFICATION

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project -- and specifier’s notes such as these.  To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1 Section Z10 Specifications and Quality sections.
************************************************************************************************************

GEnERAl

Summary

Section Includes

Two-ply atactic-polypropylene (APP) modified bituminous membrane roofing, cold applied.

Hybrid roofing system that combines built-up ply sheets with APP-modified bituminous membrane.

Substrate boards.

Roof insulation.

Vapor retarder.

Cover board.

[Section includes the installation of insulation strips in ribs of acoustical roof deck.  Insulation strips are furnished under Section 05 3000 Metal Decking.]

Related Sections

Section 06 1000, Rough Carpentry for Wood, Nailers, Curbs and Blocking.

[Section 07 0750.19, Preparation for Re-roofing.]

Section 07 6200, Sheet Metal Flashing and Trim

Section 07 7100, Roof Specialties

Section 07 9200, Joint Sealants for Joint Sealants, Joint Fillers and Joint Preparation

Section 22 1413, Facility Storm Drainage Piping for Roof Drains.

references

Definitions

Roofing Terminology: Refer to ASTM D1079 and the glossary of the National Roofing Contractors Association (NRCA) Roofing and Waterproofing Manual for definitions of roofing terms related to this section.

References

AAMA- American Architectural Manufacturer’s Association.

AAMA 2605- Voluntary Specification, Performance Requirements and Test Procedures for Superior Performing Organic Coatings on Aluminum Extrusions and Panels.

American Society of Civil Engineers (ASCE).

ASCE 7 – Minimum Design Loads for Buildings and Other Structures.

ASTM International (ASTM)

ASTM C240- Standard Test Methods of Testing Cellular Glass Insulation Block.

ASTM C552- Standard Specification for Cellular Glass Thermal Insulation.

ASTM C578- Standard Specification for Rigid, Cellular Polystyrene Thermal Insulation.

ASTM C612- Standard Specification for Mineral Fiber Block and Board Thermal Insulation.

ASTM C 726- Standard Specification for Glass Fiber/Mineral Fiber Roof Insulation Board

ASTM C 728- Standard Specification for Perlite Thermal Insulation Board.

ASTM C 1289- Standard Specification for Faced Rigid Cellular Polyisocyanurate Thermal Insulation Board.

ASTM C 1549- Standard Test Method for Determination of Solar Reflectance Near Ambient Temperature Using a Portable Solar.

ASTM D 41- Standard Specification for Asphalt Primer Used in Roofing, Dampproofing, and Waterproofing.

ASTM D 312- Standard Specification for Asphalt Used in Roofing.

ASTM D2842- Standard Test Method for Water Absorption of Rigid Cellular Plastics.

ASTM D 4586- Standard Specification for Asphalt Roof Cement, Asbestos-Free.

ASTM D 4601- Standards Specification for Asphalt-Coated Glass Fiber Base Sheet Used in Roofing.

ASTM D 5147- Standard Test Method for Sampling and Testing Modified Bituminous Sheet Materials.

ASTM D 6223- Standard Specifications for APP modified bitumen sheet materials using a combination of polyester and fiberglass reinforcements.

ASTM D 6509 – Standard specification for Atactic Polypropylene (APP) Modified Bituminous Base Sheet Materials Using Glass Fiber Reinforcements.

ASTM E 84 – Standard Test Method for Surface Burning Characteristics of Building Materials.

ASTM E 408- Standard Test Methods for Total Normal Emittance of Surfaces Using Inspection-Meter Techniques.

Factory Mutual (FM Global) – Factory Mutual Standard 4470 – Approval Standard for Class 1 Roof Covers.

Federal Specification #HH-I-1972:  Faced polyisocyanurate roof insulation board.

Green Seal: GS-36- Environmental Standard for Commercial Adhesives.

Membrane Immersion Test:  Modified Bitumen Membrane Asphaltic Impregnation Evaluation, as published in the “Proceedings of the Fourth International Symposium on Roofing Technology.”

National Roofing Contractors Association (NRCA) - Low Slope Roofing and Waterproofing Manual, Current Edition.

NBS-BSS #55:  Tensile strength for fully adhered, asphalt based roof systems.

Sheet Metal and Air Conditioning Contractors National Association, Inc, (SMACNA) - Architectural Sheet Metal Manual.

Underwriters Laboratories (UL) – Roofing Systems and Materials Guide (TGFU).

administrative requirements

Pre-installation Roofing Conference:  Conduct conference at [Project site] <Insert location>.

Meet with LANL Architect of Record, LANL’s insurer if applicable, testing and inspecting agency representative, roofing installer, roofing system manufacturer’s representative, deck installer, and installers whose work interfaces with or affects roofing, including installers of roof accessories and roof-mounted equipment.

Review methods and procedures related to roofing installation, including manufacturer’s written instructions.

Review and finalize construction schedule and verify availability of materials, installer’s personnel, equipment, and facilities needed to make progress and avoid delays.

Examine deck substrate conditions and finishes for compliance with requirements, including flatness and fastening.

Review structural loading limitations of roof deck during and after roofing.

Review base flashings, special roofing details, roof drainage, roof penetrations, equipment curbs, and condition of other construction that will affect roofing system.

Review governing regulations and requirements for insurance and certificates if applicable.

Review temporary protection requirements for roofing system during and after installation.

Review roof observation and repair procedures after roofing installation.

action SUBMITTALS / informational submittals

Product Data:  Manufacturer’s data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Roof insulation,

Manufacturer’s published specifications, base flashing details, for the specified system.

Submit Material Safety Data Sheets on all roofing materials to be used.

Shop Drawings: Provide plan section, elevation and perspective drawings as necessary to depict all flashing and project conditions on the project, including but not limited to the following:

Roof system and base flashing configuration.

Penetration details.

Termination details.

Fastening patterns.

Tapered insulation design.

Selection Samples:  For each product specified, two samples representing manufacturer’s full range of available colors and types.

Verification Samples:  For each finish product specified, two samples representing actual product, color and finish.

Manufacturer Certificates:  Signed by roofing manufacturer certifying that roofing system complies with requirements specified in “Performance Requirements” Article.

Submit evidence of complying with performance requirements.

Product Test Reports:  Based on evaluation of comprehensive tests performed by manufacturer and witnessed by a qualified testing agency, for components of membrane roofing system.

Research/Evaluation Reports:  For components of membrane roofing system, from [the ICC-ES] <Insert applicable model code organization>.

Manufacturer’s Instructions:

Manufacturer’s published installation instructions and methods.

Qualification Data:  For qualified [Installer] [manufacturer] [and] [testing agency].

sustainable design submittals

Product Test Reports for roof materials, indicating that roof materials comply with Solar Reflectance Index requirement.

Product Data for adhesives and sealants, including printed statement of VOC content.

Submit manufacturer’s documentation of Energy Star labeled roofing materials.

close-out submittals

Maintenance Data:  For roofing system to include in maintenance manuals.

Warranties:

Submit copy of the membrane manufacturer’s warranty covering materials.

Submit copy of the Roofing Subcontractor’s warranty covering workmanship.

quality assurance

Apply roofing system by an approved Subcontractor authorized prior to bid by the roof membrane manufacturer.  Prior to bid, the Roofing Subcontractor must have completed a minimum of 500 roofing squares of APP membrane in the Southwest.  To qualify for this requirement, the completed membrane must have met all conditions to obtain material and labor warranty and must be performing successfully.

Membrane manufacturer to provide a list of projects, completed in the Southwest, where the specified membrane has been in place and performing successfully for a period of not less than five (5) years. A minimum of 500 roofing squares must have been installed to meet this requirement.

Do not deviate from this specification or the approved shop drawings without prior written approval by the manufacturer and the LANL Subcontract Technical Representative (STR).

Code Requirements:  Meet the requirements of the following recognized code approval or testing agencies.  These requirements are minimum standards and no roofing work will commence without written documentation of the system’s compliance.

Underwriters Laboratories (UL) Class A membrane.

Factory Mutual (FM) 1-90 uplift rating, as indicated on Contract Documents per FM Approval Standard No. 4470.

Energy Star Roof Compliance:  Proposed roofing system will be Energy Star Roof-compliant and roofing materials will be Energy Star labeled.

For new installations, ponding must not occur in accordance with NRCA Roofing and Waterproofing Manual good roof design practice, which dictates that there will be no ponding water present 48-hours after rainfall.

There will be no more than 20 patches per 10,000 SF on new construction.

delivery, storage, and handling

Store products in manufacturer’s unopened packaging until ready for installation

Deliver roofing materials to the site in original containers, with factory seals intact

Store pail goods in their original undamaged containers in a clean, dry location within their specified temperature range.

Store roll goods on end on pallets in a clean, dry, protected area.  Do not double stack modified bitumen products.

Protect roof insulation materials from physical damage and from deterioration by sunlight, moisture, soiling, and other sources.  Store in a dry location.  Comply with insulation manufacturer’s written instructions for handling, storing, and protecting during installation.

Store and dispose of hazardous materials, and materials contaminated by hazardous materials, in accordance with requirements of local authorities having jurisdiction.

Project conditions

Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results.  Do not install products under environmental conditions outside manufacturer’s absolute limits.

Weather Limitations:  Proceed with installation only when existing and forecasted weather conditions permit roofing system to be installed according to manufacturer’s written instructions and warranty requirements.

Warranty

Special Warranty:  Manufacturer’s standard form, without monetary limitation, in which manufacturer agrees to repair  or replace components of membrane roofing system that fail in materials or workmanship within specified warranty period.

Special warranty includes membrane roofing, base flashings, [roof insulation], [fasteners], [cover boards], [substrate board] [roofing accessories] [roof pavers] and other components of membrane roofing system.

Warranty Period:  [10] [15] <Insert number> years from date of Substantial completion.

Special Project Warranty:  Submit roofing Installer’s warranty, signed by Installer, covering the Work of this Section, including all components of membrane roofing system such as membrane roofing, base flashing, roof insulation, fasteners, cover boards, substrate boards, vapor retarder, and walkway products, for the following warranty period:

Warranty Period:  [Two] <Insert number> years from date of Substantial Completion.

PRODUCTS

  - MANUFACTURERS

Manufacturers:  Subject to compliance with requirements, provide products by one of the following:

Performance Roof Systems, Inc. Specification No. -12X-FRDC.

Johns Manville Corporation Specification No. 2CIN-CA.

Performance / Design Criteria

General Performance:  Installed membrane roofing and base flashings shall withstand specified uplift pressures, thermally induced movement, and exposure to weather without failure due to defective manufacture, fabrication, installation, or other defects in construction.  Membrane roofing and base flashings shall remain watertight.

Material Compatibility:  Provide roofing materials that are compatible with one another under conditions of service and application required, as demonstrated by membrane roofing manufacturer based on testing and field experience.

Perform work in accordance with all federal, state and local codes.

Exterior Fire Test Exposure:  Provide a roofing system achieving a UL Class rating for roof slopes indicated on the Contract Drawings.

UL Class A rating.

Windstorm Classification:  Provide a roofing system which will achieve the required uplift resistance as calculated in accordance with the most current revision of ASCE 7 or as listed in the current FM Approval Guide.

90 psf of uplift resistance.

FM Rating:  Provide a roofing system which will achieve the following rating as listed in the current FM Approval Guide.

FM 1-90.

Foam Plastic Insulation:  Maximum 75/450 flame spread/smoke developed index when tested in accordance with ASTM E84.

Other Insulation:  Maximum 25/450 flame spread/smoke developed index when tested in accordance with ASTM E84.

Energy Performance:  Provide roofing system with initial Solar Reflectance Index not less than 78 when calculated according to ASTM E 1980 based on testing identical products by a qualified testing agency.

Energy Performance:  Provide roofing system that is listed on DOE’s ENERGY STAR “Roof Products Qualified Product List” for low-slope roof products.

Energy Performance:  Provide roofing system with initial Solar Reflectance not less than 0.70 and Thermal Emittance not less than 0.75 when tested according to Cool Roof Rating Council’s CRRC-1.

Manufacturer’s Requirements

Except as modified and supplemented herein, follow the Roofing Manufacturer’s and other materials manufacturer’s catalogs, general and special requirements, and specific application recommendations.

With respect to methods of installation, industry practices apply only when these specifications do not address the matter.

Slopes and Underlying Materials

Use materials which are proper for the slopes and for the underlying material to which the other materials are attached.

Roof Membrane: Mineral-surfaced, Atactic-Polypropylene (APP) modified-bitumen capsheet, ply sheet, and base sheet, and cold-applied adhesive, UL Class A, Roofing Manufacturer’s 20-year type system.

Bituminous Flashings

Composition base flashings consisting of

Ply of modified-bitumen base sheet,

Ply of mineral-surfaced modified-bitumen flashing sheet; and

Modified-bitumen flashing cement or cold-applied adhesive

Roof drain flashings consisting of:

Three-course flashing of woven glass fabric and modified-bitumen flashing cement.

Modified-bitumen membrane base sheet and ply sheet in adhesive.

Primed metal sump flashing in modified-bitumen flashing cement.

One ply of modified-bitumen ply sheet and modified-bitumen flashing cement.

Flange Strip-ins

One-ply, using modified-bitumen base sheet and modified-bitumen flashing cement.

materials

Roof Insulation

*****************************************************************************************

Select roof insulation from the following as required for compatibility with APP roofing system and applicable roof design requirements.

******************************************************************************************

General:  Preformed roof insulation boards manufactured [or approved] by roofing manufacturer, selected from manufacturer’s standard sizes and suitable for application, of thicknesses indicated [and that produces FM Approvals-approved roof insulation].

Extruded-Polystyrene Board Insulation:  ASTM C 578, [Type IV, 1.6-lb/cu.ft.] [Type X, 1.3-lb/cu.ft.] minimum density, square edged.

Molded-Polystyrene Board Insulation:  ASTM C 578 [Type II, 1.35-lb/cu.ft.] [Type VIII, 1.15-lb/cu.ft.] [Type IX, 1.8-lb/cu.ft.] minimum density.

Composite Molded-Polystyrene Board Insulation:  ASTM C 578, [Type II, 1.35-lb/cu.ft.] [Type VIII, 1.15-lb/cu.ft.] [Type IX, 1.8-lb/cu.ft.] minimum density, with factory-applied facings as follows:

Facer:  ASTM C 208, Type II, Grade 2, cellulosic-fiber insulation board, asphalt coated, ½ inch thick.

Facer:  DOC PS 2, Exposure 1, OSB, 7/16 inch thick.

Polyisocyanurate Board Insulation:  ASTM C 1289, [Type II, Class 1, Grade 2] [Type II, Class I, Grade 3], felt of glass-fiber mat facer on both major surfaces.

Composite Polyisocyanurate Board Insulation:  ASTM C 1289, with factory-applied facing board, as indicated below by type, on one major surface and felt or glass-fiber mat facer on the other surface.

Type IV, cellulosic-fiber-insulating-board facer, Grade 2, ½ inch thick.

Type V, OSB facer, 7/16 inch thick.

Type VII, glass-mat-faced gypsum board facer, ¼ inch thick.

Perlite Board Insulation:  ASTM C 728, rigid, mineral-aggregate thermal insulation board composed of expanded perlite, cellulosic fibers, binders, and waterproofing agents with top surface seal coated.

Cellulosic-Fiber Board Insulation:  ASTM C 208, Type II, Grade 2, fibrous-felted, rigid insulation boards of wood fiber or other cellulosic-fiber and water-resistant binders, asphalt impregnated, chemically treated for deterioration.

Cellular-Glass Board Insulation:  ASTM C 552, Type IV, rigid, cellular-glass thermal board insulation faced with manufacturer’s standard kraft-paper sheets.

Tapered Insulation:  Provide factory-tapered insulation boards fabricated to slope of [1/4 inch per 12 inches (1:48)] <Insert slope> unless otherwise indicated.

Provide preformed saddles, crickets, tapered edge strips, and other insulation shapes where indicated for sloping to drain.  Fabricate to slopes indicated.

Substrate Boards

******************************************************************************************

Select substrate boards from the following as required for compatibility with APP roofing system and applicable roof design requirements.

******************************************************************************************

Substrate Board:  ASTM C 1396/C 1396M, Type X gypsum board, 5/8 inch thick.

Substrate Board:  ASTM C 1177/C 1177M, glass-mat, water-resistant gypsum substrate, [1/4 inch] [1/2 inch] [Type X, 5/8 inch] thick, [factory primed].

Products:  Subject to compliance with requirements, provide the following:

          - Georgia-Pacific Corporation: [Dens Deck] [Dens Deck Prime] [Dens Deck DuraGuard].

          - <Insert manufacturer’s name; product name or designation>.

Substrate Board: ASTM C 1278/C 1278M, cellulosic-fiber-reinforced, water-resistant gypsum substrate, [1/4 inch] [3/8 inch] [1/2 inch] [5/8 inch] thick.

Products:  Subject to compliance with requirements, provide the following:

          - USG Corporation; Securock.

          - <Insert manufacturer’s name; product name or designation>.

Substrate Board:  ASTM C 728, perlite board, [3/4 inch] [1 inch] thick, seal coated.

Fasteners: Factory-coated steel fasteners and metal or plastic plates complying with corrosion-resistance provisions in FM Approvals 4470, designated for fastening substrate board to roof deck.

Vapor Retarder

******************************************************************************************

Select vapor retarder from the following as required for compatibility with APP roofing system and applicable roof design requirements.

*******************************************************************************************

Polyethylene Film:  ASTM D 4397, 6 mils thick, minimum, with maximum permeance rating of 0.13 perm.

Tape:  Pressure-sensitive tape of type recommended by vapor-retarder manufacturer for sealing joints and penetrations in vapor retarder.

Adhesive:  Manufacturer’s standard lap adhesive, FM Approvals approved for vapor-retarder application.

Laminated Sheet:  Kraft paper, two layers, laminated with asphalt and edge reinforced with woven fiberglass yarn, with maximum permeance rating of 0.50 perm [and with manufacturer’s standard adhesive].

Self-Adhering Sheet Vapor Retarder:  ASTM D 1970, minimum of 40-mil- thick, polyethylene film laminated to layer of rubberized asphalt adhesive; maximum permeance rating of 0.1 perm; cold applied, with slip-resisting surface and release paper backing.  Provide primer when recommended by vapor-retarder manufacturer.

Self-Adhering Sheet Vapor Retarder: 30 to 40-mil-thick, polyethylene film laminated to layer of butyl rubber adhesive; maximum permeance rating of 0.1 perm; cold applied, with slip-resisting surface and release paper backing.  Provide primer when recommended by vapor-retarder manufacturer.

Glass-Fiber Felt: ASTM D 2178, Type IV, asphalt impregnated.

Cover Board

*****************************************************************************************

Select cover board from the following as required for compatibility with APP roofing system and applicable roof design requirements.

******************************************************************************************

Cover Board: ASTM C 208, Type II, Grade 2, cellulosic-fiber insulation board, ½ inch thick.

Cover Board: DOC PS 2, Exposure 1, OSB, 7/16 inch thick.

Cover Board: ASTM C 1177/C 1177M, glass-mat, water-resistant gypsum substrate, [1/4 inch] [1/2 inch] [5/8 inch] thick [factory primed].

Products: Subject to compliance with requirements, provide the following:

          - Georgia-Pacific Corporation; [Dens Deck] [Dens Deck Prime] [Dens Deck DuraGuard].

          - <Insert manufacturer’s name; product name or designation>.

Cover Board:  ASTM C 1278/C 1278M, cellulosic-fiber-reinforced, water-resistant gypsum substrate, [1/4 inch] [3/8 inch] [1/2 inch] [5/8 inch] thick.

Products: Subject to compliance with requirements, provide the following:

          - USG Corporation; Securock.

          - <Insert manufacturer’s name; product name or designation>.

Insulation Accessories

General:  Furnish roof insulation accessories recommended by insulation manufacturer for intended use and compatibility with membrane roofing.

Fasteners:  Factory-coated steel fasteners and metal or plastic plates complying with corrosion-resistance provisions in FM Approvals 4470, designed for fastening roof insulation [and cover boards] to substrate, and acceptable to roofing system manufacturer.

Modified Asphaltic Insulation Adhesive:  Insulation manufacturer’s recommended modified asphaltic, asbestos-free, cold-applied adhesive formulated to attach roof insulation to substrate or to another insulation layer.

Bead-Applied Insulation Adhesive:  Insulation manufacturer’s recommended bead-applied, low-rise, one-component or multi-component urethane adhesive formulated to attach roof insulation to substrate or to another insulation layer.

Full-Spread Applied Insulation Adhesive:  Insulation manufacturer’s recommended spray-applied, low-rise, two-component urethane adhesive formulated to attach roof insulation to substrate or to another insulation layer.

Insulation Cant Strips:  ASTM C 728, perlite insulation board.

Insulation Cant Strips:  ASTM C 208, Type II, Grade 1, cellulosic-fiber insulation board.

Wood Nailer Strips:  Comply with requirements in Section 06 6100, Rough Carpentry.

Tapered Edge Strips:  ASTM C 728, perlite insulation board.

Tapered Edge Strips:  ASTM C 208, Type II, Grade 1, cellulosic-fiber insulation board.

Substrate Joint Tape:  6- or 8- inch wide, coated, glass-fiber joint tape.

Roofing Base and Ply Sheets

Smooth-surfaced, APP Modified-bitumen Base Sheet:  ASTM D 6223, Type II, Grade S:

Performance Roof Systems, Inc.  Derbigum XPS

Johns Manville Corporation Tricor™  S

Modified Bitumen Cap Sheet

Mineral-surfaced, APP Modified-bitumen Capsheet and Flashing Sheet: ASTM D 6223, Type II, Grade G, fire resistant; color white:

Performance Roof Systems, Inc.  Derbicolor XPS FR.

Johns Manville Corporation Tricor™ M FR.

Cold-applied Adhesive:

Performance Roof Systems, Inc. Permastic

Johns Manville Corporation MBR Cold Application Adhesive

Modified-bitumen Flashing Cement:

Performance Roof Systems, Inc. Perflash

Johns Manville Corporation MBR Flashing Cement

Flashing System:

Performance Roof Systems, Inc. Perflash

Johns Manville Corporation, Permaflash

Bitumen

Asphalt Bitumen:  ASTM D 312

Type III SEBS Asphalt

Concrete Primer:  As recommended by the roofing manufacturer.

Mineral Granules:  Size and color and die lot to match membrane and flashing sheets; manufactured or supplied by the Roofing Manufacturer.

Roof Walkway Pads

Mineral-surfaced, Atactic-Polypropylene, Modified-bitumen Capsheet:  ASTM D 6223, Type II, Grade G, fire resistant; color [black] [white] [select color]

Performance Roof Systems, Inc.  Derbicolor XPS FR.

Johns Manville Corporation Tricor™ M FR

Cold-applied adhesive:

Performance Roof Systems, Inc. Permastic

Johns Manville Corporation MBR Cold Application Adhesive

EXECUTION

  - EXAMINATION

Examine substrates, areas, and conditions, with Installer present, for compliance with the following requirements and other conditions affecting performance of insulation and roofing systems:

Verify that roof openings and penetrations are in place and curbs are set and braced and that roof drain bodies are securely clamped in place.

Verify that wood cants, blocking, curbs, and nailers are securely anchored to roof deck at penetrations and terminations and that nailers match thickness of insulation.

Verify that surface plane flatness and fastening of steel roof deck complies with requirements in Section 05 3000 Metal Decking.

Verify that minimum concrete drying period recommended by roofing system manufacturer has passed.

Verify that concrete substrate is visibly dry and free of moisture.  Test for capillary moisture by plastic sheet method according to ASTM D 4263.

Test for moisture by pouring 1 pint of hot roofing asphalt on deck at start of each day’s work and at start of each roof area or plane.  Do not proceed with roofing work if test sample foams or can be easily and cleanly stripped after cooling.

Verify that concrete-curing compounds that will impair adhesion of roofing components to roof deck have been removed.

Verify that deck is securely fastened with no projecting fasteners and with no adjacent units in excess of 1/16 inch out of plane relative to adjoining deck.

Proceed with installation only after unsatisfactory conditions have been corrected.

PREPARATION

Clean substrate of dust, debris, moisture, and other substances detrimental to insulation and roofing installation according to roofing system manufacturer’s written instructions.  Remove sharp projections.

Prevent materials from entering and clogging roof drains and conductors and from spilling or migrating onto surfaces of other construction.  Remove roof-drain plugs when no work is taking place or when rain is forecast.

Prime surface of concrete deck with asphalt primer as recommended by roofing manufacturer and allow primer to dry.

substrate board INSTALLATION

Install substrate board with long joints in continuous straight lines, perpendicular to roof slopes with end joints staggered between rows. Tightly butt substrate boards together.

Fasten substrate board to top flanges of steel deck according to recommendations in FM Approval Guide for specified Windstorm Resistance Classification.

Fasten substrate board to top flanges of steel deck to resist uplift pressure at corners, perimeter, and field of roof according to membrane roofing system manufacturers’ written instructions.

vapor-retarder Installation

**************************************************************************************************

Select vapor-retarder installation method as required for selected vapor-retarder.

**************************************************************************************************

Polyethylene Film:  Loosely lay polyethylene-film vapor retarder in a single layer over area to receive vapor retarder, side ad end lapping each sheet a minimum of 2 inches and 6 inches, respectively.

Continuously seal side and end laps with [tape] [adhesive].

Laminate sheet:  Install laminate-sheet vapor retarder in a single layer over area to receive vapor retarder, side and end lapping each sheet a minimum of 2 inches and 6 inches, respectively.  Bond vapor retarder to substrate as follows:

Apply adhesive at rate recommended by vapor-retarder manufacturer.  Seal laps with adhesive.

Apply ribbons of hot roofing asphalt at spacing, temperature, and rate recommended by vapor-retarder manufacturer.  Seal laps with hot roofing asphalt.

Self-Adhering Sheet Vapor Retarder:  Prime substrate if required by manufacturer.  Install self-adhering sheet vapor retarder over area to receive vapor retarder, side and end lapping each sheet a minimum of 3-1/2 inches and 6 inches, respectively.  Seal laps by rolling.

Built-up Vapor Retarder:  Install two-glass-fiber felt plies lapping each felt 19 inches over preceding felt. Embed each felt in a solid mopping of hot roofing asphalt.  Glaze-coat completed surface with hot roofing asphalt. Apply hot roofing asphalt within plus or minus 25 deg F of equiviscous temperature.

Completely seal vapor retarder at terminations, obstructions, and penetrations to prevent air movement into membrane roofing system.

Insulation installation

**************************************************************************************************

Select insulation installation method as required for selected insulation.

**************************************************************************************************

Comply with roofing system manufacturer’s written instructions for installing roof insulation.

Install one lapped base-sheet course and mechanically fasten to substrate according to roofing system manufacturer’s written instructions.

Nailer Strips:  Mechanically fasten 4-inch nominal (89-mm actual) width wood nailer strips of same thickness as insulation perpendicular to sloped roof deck at the following spacing:

[16 feet] <Insert spacing> apart for roof slopes steeper than 1 inch per 12 inches (1:12) but less than 3 inches per 12 inches (3:12).

[48 inches] <Insert spacing> apart for roof slopes steeper than 3 inches per 12 inches (3:12).

Insulation Cant Strips:  Install and secure preformed 45-degree insulation cant strips at junctures of roofing membrane system with vertical surfaces or angle changes more than 45 degrees.

Install tapered insulation under area of roofing to conform to slopes indicated.

Install insulation with long joints of insulation in a continuous straight line with end joints staggered between rows, abutting edges and ends between boards.  Fill gaps exceeding ¼ inch with insulation.

Cut and fit insulation within ¼ inch of nailers, projections, and penetrations.

Install insulation under area of roofing to achieve required thickness.  Where overall insulation thickness is 2.7 inches or more, install two or more layers with joints of each succeeding layer staggered from joints of previous layer a minimum of 6 inches in each direction.

Where installing composite and non-composite insulation in two or more layers, install non-composite board insulation for bottom layer and intermediate layers, if applicable, and install composite board insulation for top layer.

Trim surface of insulation where necessary at roof drains so completed surface is flush and does not restrict flow of water.

Install tapered edge strips at perimeter edges of roof that do not terminate at vertical surfaces.

Adhered Insulation:  Install each layer of insulation and adhere to substrate as follows:

Prime surface of concrete deck with asphalt primer at rate of ¾ gal./100 sq.ft. and allow primer to dry.

Set each layer of insulation in a solid mopping of hot roofing asphalt applied within plus or minus 25 deg F of equiviscous temperature.

Set each layer of insulation in ribbons of bead-applied insulation adhesive, firmly pressing and maintaining insulation in place.

Set each layer of insulation in a uniform coverage of full-spread insulation adhesive, firmly pressing and maintaining insulation in place.

Mechanically Fastened Insulation:  Install each layer of insulation and secure to deck using mechanical fasteners specifically designed and sized for fastening specified board-type roof insulation to deck type.

Mechanically fasten insulation to substrate with fasteners/plates and pattern complying with FM 1-90 requirements and approved by membrane manufacturer.

Fasten insulation to resist uplift pressure of corners, perimeter, and field of roof.

Mechanically Fastened and Adhered Insulation:  Install first layer of insulation to deck using mechanical fasteners specifically designed and sized for fastening specified board-type roof insulation to deck type.

Mechanically fasten insulation to substrate with fasteners/plates and pattern complying with FM 1-90 requirements and approved by membrane manufacturer.

Fasten first layer of insulation to resist uplift pressure at corners, perimeter, and field of roof.

Set each subsequent layer of insulation in a solid mopping of hot roofing asphalt applied within plus or minus 25 deg F of equiviscous temperature.

Set each subsequent layer of insulation in ribbons of bead-applied insulation adhesive, firmly pressing and maintaining insulation in place.

Set each subsequent layer of insulation in a uniform coverage of full-spread insulation adhesive, firmly pressing and maintaining insulation in place.

Cover board installation

Install cover boards over insulation with long joints in continuous straight lines with end joints staggered between rows.  Offset joints a minimum of 6 inches in each direction from joints of insulation below.  Loosely butt cover boards together [and fasten to roof deck].  Tape joints if required by roofing system manufacturer.

Fasten cover boards according to requirements in FM Approvals’ “RoofNav” for specified Windstorm Resistance Classification.

Fasten cover boards to resist uplift pressure at corners, perimeter, and field of roof.

Apply hot roofing asphalt to underside, and immediately bond cover board to substrate.

roofing membrane installation, general

Install roofing membrane system according to roofing system manufacturer’s written instructions and applicable recommendation in ARMA/NRCA’s “Quality Control Guidelines for the Application of Polymer Modified Bitumen Roofing” and as follows:

Deck type:  [N (nailable)] [I (insulated)] [C (concrete or nonnailable)].

Adhering Method: L (cold-applied adhesive).

Base Sheet: One

Number of Glass-Fiber Base-Ply Sheets: One.

Number of APP-Modified Asphalt Sheets: One.

Surfacing Type: [S (smooth)] [M (mineral-granule-surfaced cap sheet)].

Start installation of roofing membrane in presence of roofing system manufacturer’s technical personnel.

Where roof slope exceeds [1/2 inch per 12 inches (1:24)] [3/4 inch per 12 inches (1:18)] <Insert slope>, install roofing membrane sheets parallel with slope.

Backnail roofing membrane sheets to [nailer strips] [substrate] according to roofing system manufacturer’s written instructions.

Cooperate with testing agencies engaged or required to perform services for installing roofing system.

Coordinate installation of roofing system so insulation and other components of the roofing membrane system not permanently exposed are not subjected to precipitation or left uncovered at the end of the workday or when rain is forecast.

At end of each day’s work, provide tie-offs to cover exposed roofing membrane sheets and insulation with a course of coated felt set in roofing cement or hot roofing asphalt, with joints and edges sealed.

Complete terminations and base flashings and provide temporary seals to prevent water from entering completed sections of roofing system.

Remove and discard temporary seals before beginning work on adjoining roofing.

Substrate-Joint Penetrations:  Prevent roofing asphalt and adhesives from penetrating substrate joints, entering building, or damaging roofing system components or adjacent building construction.

base-ply sheet installation

Install base sheets according to roofing system manufacturer’s written instructions starting at low point of roofing system.  Align base sheets without stretching. Extend sheets over and terminate beyond cants

Shingle side laps of base sheets uniformly to ensure that required number of base sheets covers substrate at any point.  Shingle in direction to shed water.

Embed each base sheet in a continuous void-free mopping of hot roofing asphalt to form a uniform membrane without base sheets touching.

app-modified bituminous membrane installation

Install modified bituminous roofing membrane cap sheet according to roofing manufacturer’s written instructions, starting at low point of roofing system.  Extend roofing membrane sheets over and terminate beyond cants, installing as follows:

Adhere to substrate in cold-applied adhesive.

Torch apply to substrate.

Unroll roofing membrane sheets and allow them to relax for minimum time period required by manufacturer.

Laps:  Accurately align roofing membrane sheets, without stretching, and maintain uniform side and end laps.  Stagger end laps.  Completely bond and seal laps, leaving no voids.

Repair tears and voids in laps and lapped seams not completely sealed.

Apply roofing granules to cover exuded bead at laps while bead is hot.

Install roofing membrane sheets so side and end laps shed water.

Flashing and stripping installation

Install base flashing over cant strips and other sloped and vertical surfaces, at roof edges, and at penetrations through roof; secure to substrates according to roofing system manufacturer’s written instructions, and as follows:

Prime substrates with asphalt primer if required by roofing system manufacturer.

Backer Sheet Application:  Mechanically fasten backer sheet to walls or parapets.  Adhere backer sheet over roofing membrane at cants in cold-applied adhesive.

Backer Sheet Application: Adhere backer sheet to substrate in cold-applied adhesive at rate required by roofing system manufacturer.

Flashing Sheet Application:  Adhere flashing sheet to substrate in flashing cement at rate required by roofing system manufacturer.

Extend base flashing up walls or parapets a minimum of [8 inches] above roofing membrane and [4 inches] onto field of roofing membrane.

Mechanically fasten top of base flashing securely at terminations and perimeter of roofing.

Seal top termination of base flashing with a strip of glass-fiber fabric set in asphalt roofing cement.

Install roofing membrane cap-sheet stripping where metal flanges and edgings are set on membrane roofing according to roofing system manufacturer’s written instructions.

Metal Counter Flashing:  Cover all vertical base flashings with metal counter flashing to form a continuous water shedding surface over the top of membrane flashing.  Extend metal counter flashing a minimum of 3 inches (76 mm) over the top of the membrane flashing.

Metal Face Securement:  Install hook strips (cleats) on all metal extending over roof edges (coping metal, gravel stop/eave strip, perimeter curb metal, etc.) in accordance with recommendations in the NRCA Roofing and Waterproofing Manual.  Appropriate provision must be made in accessory metal to allow for expansion and contraction of the metal sections without interrupting the integrity of the waterproofing assembly.

Roof Drains:  Set [30-by-30-inch] <Insert size> square metal flashing in bed of roofing-manufacturer-approved asphaltic adhesive on completed roofing membrane.  Cover metal flashing with roofing membrane cap-sheet stripping and extend a minimum of [4 inches] [6 inches] beyond edge of metal flashing onto field of roofing membrane.  Clamp roofing membrane, metal flashing, and stripping into roof-drain clamping ring.

Install stripping according to roofing system manufacturer’s written instructions.

coating installation

Apply coating to [roofing membrane] [and] [base flashings] according to manufacturer’s written instructions, by spray, roller, or other suitable application method [to provide a dry film thickness of not less than 20 mils].

walkway installation

Walkway Pads:  Install walkway pads in cold-applied adhesive, using units of size indicated, or if not indicated, of manufacturer’s standard size according to walkway manufacturer’s written instructions.

Walkway strips:  Install walkway [backer and] cap sheet strips over roofing membrane using same application method as used for roofing membrane cap sheet.

field quality control

Testing agency:  Owner will engage a qualified testing agency to perform tests and inspections and to prepare test reports.

Test Cuts:  Test specimens will be removed to evaluate problems observed during quality-assurance inspections of roofing membrane as follows:

Approximate quantities of components within roofing membrane will be determined according to ASTM D 3617.

Test specimens will be examined for interplay voids according to ASTM D 3617 and to comply with criteria established in Appendix 3 in ARMA/NRCA’s “Quality Control Guidelines for the Application of Polymer Modified Bitumen Roofing.”

Repair areas where test cuts were made according to roofing system manufacturer’s written instructions.

Final Roof Inspection:  Arrange for roofing system manufacturer’s technical personnel to inspect roofing installation on completion.

Notify LANL STR 48 hours in advance of date and time of inspection.

Roofing system will be considered defective if it does not pass tests and inspections.

Additional testing and inspecting, at Construction Subcontractors expense will be performed to determine if replaced or additional work complies with specified requirements.

protecting and cleaning

Do not leave installed insulation exposed to weather.  Cover and waterproof immediately after installation.

Temporarily seal exposed insulation edges at the end of each day by lapping roofing membrane over edge to form a seal.  Remove seal when Work resumes.

Remove installed insulation that has become wet or damaged and replace the new insulation material.

Protect insulation from traffic with protective covering materials during and after installation.

Protect roofing system from damage and wear during remainder of construction period.  When remaining construction will not affect or endanger roofing, inspect roofing for deterioration and damage, describing its nature and extent in a written report, with copies to LANL STR.

Correct deficiencies in or remove roofing system that does not comply with requirements, repair substrates, and repair or reinstall roofing system to a condition free of damage and deterioration at time of Substantial completion and according to warranty requirements.

Clean overspray and spillage from adjacent construction using cleaning agents and procedures recommended by manufacturer of affected construction.

Maintain job site in a clean, orderly fashion, and free of debris.  Store materials and equipment so operations of building are not interrupted.

END OF SECTION

******************************************************************

Do not delete the following reference information:

******************************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 07 5213.13 Rev. 0, dated March 8, 2010.