SECTION 08 3100

ACCESS DOORS AND PANELS

*************************************************************************************************************

LANL MASTER SPECIFICATION

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project -- and specifier’s notes such as these.  To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1 Section Z10 Specifications and Quality sections.
*************************************************************************************************************

PART 1	GENERAL

1.1	SECTION INCLUDES

A.	Ceiling and wall mounted, non-rated access door and frame units.

1.2	SUBMITTALS

A.	Submit the following in accordance with the requirements of Section 01 3300, Submittal Procedures:

1.	Catalog data which includes sizes, types, finishes, and details of adjoining work.

- Manufacturer's Installation Instructions and rough-in dimensions.

- Schedule:  Types, locations, sizes, latching or locking provisions, and other data pertinent to installation.

PART 2	PRODUCTS

2.1	ACCEPTABLE MANUFACTURERS

A.	Cesco Products

B.	J. L. Industries

C.	Milcor

2.2	FABRICATION

A.	Fabricate frames and flanges of 16 gauge steel.

B.	Fabricate door panels of 20 gauge steel with integral non-combustible insulation filler.

********

or

********

C.	Fabricate door panels of 14 gauge steel (non-insulated)]

D.	Weld, fill, and grind joints to assure flush and square unit.

E.	Hardware:

1.	Hinge:  175 degree steel hinges with removable pins.

2.	Lock:  Screw driver slot for quarter turn cam lock.

2.3	FINISHES

A.	Base Metal Protection:  Prime coat units with baked on primer.

B.	Finish:  Two coats acrylic enamel, white color or match adjoining color where exposed.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Verify that rough openings are correctly sized and located.

3.2	INSTALLATION

A.	Install units in accordance with manufacturer's instructions.

B.	Install frames plumb and level in openings.  Secure rigidly in place.

C.	Position unit to provide convenient access to concealed work requiring access.

end of section

*************************************************************************

Do not delete the following reference information:

*************************************************************************

for lanl use only

This project specification is based on LANL Master Specification 08 3100 Rev. 2, dated May 12, 2008.