SECTION 09 2913

GYPSUM ROOF BOARD

## *************************************************************************************************************

LANL MASTER SPECIFICATION

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project -- and specifier’s notes such as these.  To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1 Section Z10 Specifications and Quality sections.

*************************************************************************************************************

# PART 1 – GENERAL

## 1.1	DESCRIPTION

A.	Work in this section includes, but is not limited to:

1.	Thermal barrier.

2.	Roofing protection board.

3.	Roof insulation protection board.

4.	Formboard for gypsum concrete.

5.	Re-cover board.

B.	Related work specified elsewhere:

1.	Roof insulation.

2.	Roof membrane.

## 1.2	SUBMITTALS

A.	Product data: Submit manufacturer’s descriptive literature indicating material composition, thickness, sizes and fire resistance.

B.	Shop drawings: Submit shop drawings indicating fastener and adhesive patterns for Factory Mutual Engineering & Research Corporation (FMERC) wind uplift resistance specified.

C.	Certification: Submit manufacturer’s written certification that product meets fire-resistance requirements.

## 1.3	DELIVERY, STORAGE AND HANDLING

A.	Delivery: Deliver materials to the job site in manufacturer’s original packaging, containers and bundles with manufacturer’s brand name and identification intact and legible.

- Storage and handling: Roof board must be kept dry before, during and after application. Outside storage must be off ground and protected by a breathable waterproof covering. If roof board becomes wet, it must be dried before installation. Roof board must be roofed the same day it is installed.

- Consult membrane manufacturer for specific installation instructions and standards for good roofing practices.

## 1.4	LIMITATIONS

A.	Panels must be kept dry before, during and after installation. Apply only as much roof board as can be covered by a roof membrane system in the same day.

- When applying solvent-based adhesives or primers, allow sufficient time for the solvent to flash off to avoid damage to roofing components.

C.	Consult membrane manufacturer for specific system installation needs.

# PART 2 – PRODUCTS

## 2.1	GYPSUM ROOF BOARD

A.	Dens-Deck  (Or Equal)

1.	Acceptable product: G-P Gypsum Corporation Dens-Deck roof board, acceptable to membrane manufacturer.

2.	Composition: Nonstructural, glass mat faced gypsum panel with water-resistant core.

3.	Size: Nominal 4’ x 8’.

4.	Thickness: ½”.

## 2.2	MISCELLANEOUS MATERIALS

A.	Adhesives: As recommended by roof system manufacturer

# PART 3 – EXECUTION

## 3.1	GENERAL

- Provide roof board where indicated on drawings using adhesive system specified.

- Accumulation of water due to leaks or condensation in or on roof board must be avoided during construction and after construction. Avoid overuse of non-vented, direct-fired heaters during winter months. Avoid application of roof board during rain, heavy fogs and other conditions that may deposit moisture on the surface.

## 3.2	GYPSUM ROOF BOARD INSTALLATION

A.	Adhered Systems: Single component elastomeric, low rise urethane foam adhesive that contains no solvents as recommended by roof system and adhesive manufacturers.

B.	Wind uplift/FMERC compliance for adhered attachment to achieve accordance with J.I. 1N2A6.AM of FMRC Standard 4450 for FM I-90. Refer to membrane manufacturer’s system recommendations.

END OF SECTION

****************************************************************

Do not delete the following reference information.

****************************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 09 2913 Rev. 1, dated May 14, 2008.