# SECTION 09 6513

# RESILIENT BASE AND ACCESSORIES

*************************************************************************************************************

LANL MASTER SPECIFICATION

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project -- and specifier’s notes such as these.  To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1 Section Z10 Specifications and Quality sections.
*************************************************************************************************************

PART 1	GENERAL

# 1.1	SECTION INCLUDES

A.	Resilient base at carpet and resilient flooring finishes.

# 1.2	REGULATORY REQUIREMENTS

A.	Conform to applicable code for flame/fuel/smoke rating requirements of ASTM E84.

B.	40 CFR 247 Comprehensive Procurement Guidelines for Products Containing Recovered Materials.

# 1.3	ENVIRONMENTAL REQUIREMENTS

A.	Store materials in area of installation for three days prior to installation to achieve temperature stability.

B.	Maintain ambient temperature required by adhesive manufacturer three days prior to, during, and 24 hours after installation of materials.

# 1.4	SUBMITTALS

A.	Submit the following in accordance with Section 01 3300, Submittal Procedures.

- Product data for [approval] [information] of the resilient base.

2.	Manufacturer’s installation instructions.

3.	Provide samples of color range specified or offered by the manufacturer.

4.	Cleaning and maintenance information.

- Certification that recovered (recycled) materials is 90 to 100 percent per 40 CFR 247 requirements.

- Manufacturer’s certification of asbestos-free products for all products including adhesives and mastics.

PART 2	PRODUCTS

# 2.1	PRODUCT OPTIONS AND SUBSTITUTIONS

# A.	Comply with Section 01 2500, Substitution Procedures.

# 2.2	ACCEPTABLE MANUFACTURERS - BASE MATERIALS

A.	Burke Flooring Products.

B.	Flexco Company.

C.	Roppe.

# 2.3	BASE MATERIALS

A.	Provide base conforming to FS SS-W-40:  Type I rubber; provide roll stock for distances 8 feet or greater, 4 inches high; 1/8 inch thick; top set coved; color will be selected by LANL from the manufacturer’s standard samples.

# 2.4	ACCESSORIES

A.	Provide primers and adhesives that are waterproof, and of type recommended by manufacturer.

PART 3	EXECUTION

# 3.1	EXAMINATION

A.	If substrate conditions will adversely affect acceptable results , do not begin installation and notify the LANL Subcontract Technical Representative (STR) .

# 3.2	INSTALLATION - BASE MATERIAL

A.	Fit joints tight and vertical.  Maintain minimum measurement of 18 inches between joints.

B.	Miter internal corners.  At external corners, "V" cut back of base strip to 2/3 of its thickness and fold.

C.	Install base on solid backing.  Bond tight to wall and floor surfaces.

D.	Scribe and fit to door frames and other interruptions.

# 3.3	CLEANING

A.	Remove excess adhesive from floor, base, and wall surfaces without damage to those surfaces.

# END OF SECTION

*****************************************************************

Do not delete the following reference information:

*****************************************************************

# FOR LANL USE ONLY

This project specification is based on LANL Master Specification 09 6513 Rev. 1, dated May 14, 2008.