SECTION 02 3000

SUBSURFACE INVESTIGATION

************************************************************************************************************************

LANL MASTER SPECIFICATION

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project -- and specifiers notes such as these.  To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual (ESM) Structural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1 Section Z10 Specifications and Quality sections.

************************************************************************************************************************

general

section includes

LANL furnished soils investigation report.

DESCRIPTION

A soils investigation report titled [REPORT NAME AND NUMBER], dated [REPORT DATE], has been prepared for the site of this work by [NAME OF COMPANY] and is available from the Subcontract Administrator.

Such information is not a warranty of subsurface conditions and may not reflect subsurface conditions over the entire proposed construction area.  The Subcontractor shall be responsible for his/her interpretations and use of the information.  Also note General Provision "Site Investigation and Conditions Affecting the Work."

The availability or use of the soils investigation report and logs of test borings shall not be construed as a waiver of the Subcontractor's duty to examine the site and the conditions affecting the work, and does not relieve the Subcontractor from the risk of soil or subsurface conditions which could reasonably be anticipated or from properly fulfilling the terms of the Subcontract.

PRODUCTS

Not Used

EXECUTION

Not Used

END OF SECTION

*****************************************************************

Do not delete the following reference information:

*****************************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 02 3000 Rev. 1, dated April 23, 2008.