SECTION 09 2913

GYPSUM ROOF BOARD

## *************************************************************************************************************

LANL MASTER SPECIFICATION

When editing to suit project, author shall add job-specific requirements and delete only those portions that in no way apply to the activity (e.g., a component that does not apply). To seek a variance from applicable requirements, contact the ESM Architectural POC.

When assembling a specification package, include applicable specifications from all divisions, especially Division 1, General Requirements.

Delete information within “stars” during editing.

Specification developed for ML-3 / ML-4 projects. For ML-1 / ML-2, additional requirements and QA reviews are required.

*************************************************************************************************************

# PART 1 – GENERAL

## 1.1	DESCRIPTION

A.	Work in this section includes, but is not limited to:

1.	Thermal barrier.

2.	Roofing protection board.

3.	Roof insulation protection board.

4.	Formboard for gypsum concrete.

5.	Re-cover board.

B.	Related work specified elsewhere:

1.	Roof insulation.

2.	Roof membrane.

## 1.2	SUBMITTALS

A.	Product data: Submit manufacturer’s descriptive literature indicating material composition, thickness, sizes and fire resistance.

B.	Shop drawings: Submit shop drawings indicating fastener and adhesive patterns for Factory Mutual Engineering & Research Corporation (FMERC) wind uplift resistance specified.

C.	Certification: Submit manufacturer’s written certification that product meets fire-resistance requirements.

## 1.3	DELIVERY, STORAGE AND HANDLING

A.	Delivery: Deliver materials to the job site in manufacturer’s original packaging, containers and bundles with manufacturer’s brand name and identification intact and legible.

- Storage and handling: Roof board must be kept dry before, during and after application. Outside storage must be off ground and protected by a breathable waterproof covering. If roof board becomes wet, it must be dried before installation. Roof board must be roofed the same day it is installed.

- Consult membrane manufacturer for specific installation instructions and standards for good roofing practices.

## 1.4	LIMITATIONS

A.	Panels must be kept dry before, during and after installation. Apply only as much roof board as can be covered by a roof membrane system in the same day.

- When applying solvent-based adhesives or primers, allow sufficient time for the solvent to flash off to avoid damage to roofing components.

C.	Consult membrane manufacturer for specific system installation needs.

# PART 2 – PRODUCTS

## 2.1	GYPSUM ROOF BOARD

A.	Dens-Deck  (Or Equal)

1.	Acceptable product: G-P Gypsum Corporation Dens-Deck roof board, acceptable to membrane manufacturer.

2.	Composition: Nonstructural, glass mat faced gypsum panel with water-resistant core.

3.	Size: Nominal 4’ x 8’.

4.	Thickness: ½”.

## 2.2	MISCELLANEOUS MATERIALS

A.	Adhesives: As recommended by roof system manufacturer

# PART 3 – EXECUTION

## 3.1	GENERAL

- Provide roof board where indicated on drawings using adhesive system specified.

- Accumulation of water due to leaks or condensation in or on roof board must be avoided during construction and after construction. Avoid overuse of non-vented, direct-fired heaters during winter months. Avoid application of roof board during rain, heavy fogs and other conditions that may deposit moisture on the surface.

## 3.2	GYPSUM ROOF BOARD INSTALLATION

A.	Adhered Systems: Single component elastomeric, low rise urethane foam adhesive that contains no solvents as recommended by roof system and adhesive manufacturers.

B.	Wind uplift/FMERC compliance for adhered attachment to achieve accordance with J.I. 1N2A6.AM of FMRC Standard 4450 for FM I-90. Refer to membrane manufacturer’s system recommendations.

END OF SECTION

****************************************************************

Do not delete the following reference information.

****************************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification Rev. 0, dated February 24, 2006.