SECTION 10 2800

TOILET, BATH, AND LAUNDRY ACCESSORIES

*************************************************************************************************************

LANL MASTER SPECIFICATION

When editing to suit project, author shall add job-specific requirements and delete only those portions that in no way apply to the activity (e.g., a component that does not apply).  To seek a variance from applicable requirements, contact the Engineering Standards Manual (ESM) Architectural POC.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General Requirements.

Delete information within “stars” during editing.

Specification developed for ML-3 / ML-4 projects.  For ML-1 / ML-2, additional requirements and QA reviews are required.

*************************************************************************************************************

GENERAL

SECTION INCLUDES

Toilet accessories and their associated fasteners and hardware.

QUALITY ASSURANCE

Furnish inserts and anchoring devices which must be set in concrete or built into masonry. Coordinate delivery with other Work to avoid delay.

Coordinate accessory locations with other Work to avoid interference and to assure proper operation and servicing of accessory units.

Provide all accessories manufactured by the same company, except for soap dispenser, which must accommodate “Sani-Fresh” soap cartridges.

SUBMITTALS

Submit the following in accordance with Section 01 3300, Submittal Procedures:

Catalog data.

Manufacturer’s installation instructions.

PRODUCTS

  - PRODUCT OPTIONS AND SUBSTITUTIONS

    - Alternate products may be accepted; follow Section 01 2500, Substitution Procedures.

  - MATERIALS, GENERAL

    - Use stainless steel complying with ANSI Type 302/304, with polished No. 4 finish, 22 gage (0.34 inch) minimum, unless otherwise indicated.

    - Use leaded and unleaded brass, flat products, complying with FS QQ-B-613; rods, shapes, forgings and flat products with finished edges, FS QQ-B-62.

    - Use commercial quality, cold rolled, sheet steel complying with ASTM A366, 20 gage (0.040 inch) minimum, unless otherwise indicated. Provide surface preparation and metal pretreatment as required for applied finish.

    - Use galvanized steel sheet complying with ASTM A527, G60.

    - Use base metal with nickel and chromium electrodeposited in compliance with ASTM B456, Type SC2.

    - Use galvanized steel mounting devices complying with ASTM A153, hot dip galvanized after fabrication.

    - Use screws, bolts, and other devices of same materials as accessory unit or of galvanized steel where concealed.

    - Use 1/4 inch thick, Type l, Class 1, Quality q2, mirror glass conforming to FS DD-G-451, with silvering, copper coating, and protective organic coating complying with FSS DD-M-411.

  - MANUFACTURERS

    - Bradley Corporation

    - Bobrick Washroom Equipment Co.

    - AJ Washroom Accessories

    - American Specialties Inc. (ASII)

  - COMBINATION TOWEL DISPENSER/WASTE RECEPTACLE UNIT

    - Semi-recessed unit with extended waste receptacle.  Provide stainless steel unit made for 4 inch over-all depth, with continuous 1 inch wall flange.  Provide towel dispenser in top of unit, designed for standard core 8 inch or 9 inch wide, 800 feet long.  Provide waste receptacle in bottom of unit.  Bobrick Model B-3966, Bradley Model 227-10.  Symbol PTD.

  - SANITARY NAPKIN DISPENSER

    - Provide surface mounted, stainless steel unit that dispenses both napkins and tampons, coin free. Provide dispensing identification of “Napkins” and “Tampons”.  Bobrick Model B-254, Bradley Model 426.  Symbol SND.

  - SANITARY NAPKIN RECEPTACLE

    - Provide surface mounted, stainless steel unit with self-closing door.  Bobrick Model B-254, Bradley Model 4722-15.  Symbol SNR.

  - TOILET SEAT COVER DISPENSER

    - Provide surface mounted, stainless steel unit with hinged access door for refilling.  Bobrick Model B-221, Bradley Model 583.  Symbol TSCD.

  - GRAB BARS

    - Provide 1 1/4 inch OD, stainless steel grab bars with mounting flanges with concealed fasteners.  Provide 1 1/2 inch clearance from bar to wall.  Provide textured gripping surface.  Bobrick Model B-550 Series, Bradley Model 893 Series.  Symbol GB.

  - SOAP DISPENSER

    - Provide stainless steel, recessed liquid soap dispenser unit. ASI Model 5002, AJ Model U102.  Symbol SD.

  - TOILET PAPER DISPENSER

    - Provide stainless steel, surface mounted dispenser for two rolls, with shelf.  Bobrick Model B-2840, Bradley Model 5263.  Symbol TPD.

  - MIRROR

    - Provide stainless steel framed mirror with 1/4 inch plate glass mirror.  Bobrick Model B-290 Series, Bradley Model 700 Series.  Symbol M.

  - SHELF

    - Provide stainless steel, wall mounted shelf, 6 inches wide by 24 inches long.  Bobrick Model B-296, Bradley Model 756.  Symbol S.

  - MOP AND BROOM HOLDER

    - Provide stainless steel, wall mounted combination mop and broom holder.  Bobrick Model B-223x24, Bradley Model 9953.  Symbol MBH.

  - COAT HOOK

    - Provide stainless steel coat hooks on inside face of toilet compartment doors.  Bobrick Model B-682, Bradley Model 9134.  Symbol CH.

  - LOCKS

    - Provide accessories without keyed locks.  Modify accessories with locks as standard features to perform as latches only.

  - FABRICATION

    - Only an unobtrusive stamped logo of the manufacturer is permitted on exposed faces of the units.  In an unexposed location, place the manufacturer’s name and product model number.

    - Fabricate units with welded and ground joints and edges rolled.  Hang doors with continuous stainless steel piano hinges.  Provide for concealed anchorage wherever possible.

    - Mirror fabrication:

      - Fabricate frames to accommodate wood, felt, plastic, or other glass edge protection material.

      - Provide galvanized steel backing sheet, no less than 22 gage and full mirror size, with non-absorptive filler material.  Corrugated cardboard is not an acceptable filler material.

      - Provide hanger system for tamperproof installation, using galvanized steel wall brackets with concealed locking devices requiring a special tool to remove.

**************************************************************************************

Provide a schedule if job requires one.

SCHEDULE

Men’s Toilet

Women’s Toilet

Janitor’s Closet

****************************************************************************************

EXECUTION

  - iNSTALLATION

    - Install accessories in accordance with approved manufacturer’s installation instructions.

    - Securely attach each accessory, level and plumb, at locations shown on the Drawings and at heights, spacing, and load resistance required by ADAAG (Americans with Disabilities Act Accessibility Guidelines.

    - Use fasteners that are appropriate for surfaces where accessories are to be mounted.

    - Use concealed fasteners wherever possible.

    - Secure mirrors in a tamperproof manner.

  - CLEANING

    - Clean stainless steel and mirror surfaces in compliance with manufacturer’s instructions.

END OF SECTION

*****************************************************************

Do not delete the following reference information:

*****************************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 10 2800 Rev. 0, dated 
January 6, 2006.