SECTION 10 5113

METAL LOCKERS

****************************************************************************************************

LANL MASTER SPECIFICATION

This template must be edited for each project.  In doing so, specifier must add job-specific requirements.  Brackets are used in the text to indicate designer choices or locations where text must be supplied by the designer.  Once the choice is made or text supplied, remove the brackets.  The specifications must also be edited to delete specification requirements for processes, items, or designs that are not included in the project -- and specifier’s notes such as these.  To seek a variance from requirements in the specifications that are applicable, contact the Engineering Standards Manual Architectural POC. Please contact POC with suggestions for improvement as well.

When assembling a specification package, include applicable specifications from all Divisions, especially Division 1, General requirements.

Specification developed for ML-4 projects.  For ML-1, 2, and 3 applications, additional requirements and independent reviews should be added if increased confidence in procurement or execution is desired; see ESM Chapter 1 Section Z10 Specifications and Quality sections.

****************************************************************************************************

PART 1  GENERAL

1.1	SECTION INCLUDES

A.	Locker units with hinged doors

B.	Metal bases, tops and filler panels

1.2	SUBMITTALS

A.	Submit the following in accordance with the requirements of Section 01 3300.

1.	Catalog data indicating locker types, sizes and accessories.

2.	Color chart indicating manufacturer’s standard colors.

3.	Manufacturer’s installation instructions.

4.	Shop drawing indicating locker plan layout.

PART 2  PRODUCTS

2.1	MANUFACTURERS

A.	DeBourgh Manufacturing, Varsity Series

B.	Interior/Medart, Fortress Series

C.	Lyon Metal Products, Inc., Industrial Series

2.2	MATERIALS

A.	Use mild, cold rolled and leveled unfinished sheet steel, with the following 			thicknesses:

1.	Body sides and bottoms:  16 gage

2.	Body back:  18 gage

3.	Door:  14 gage

4.	Door frame:  16 gage

5.	Sloping top:  14 gage

2.3	ACCESSORIES

A.	Provide for each locker:

1.	Two double prong coat hooks

2.	Hat shelf

3.	Rubber bumpers

4.	Combination lock

2.4	FABRICATION

A.	Locker units

1.	Width:  [ 12   15   18 ] inches

2.	Depth:  [ 12   15   18 ] inches

3.	Height:  72 inches

4.	Mounting:  [Surface mounted   Freestanding }

5.	Base:  4 inch high metal

6.	Top:  sloping metal with closures

7.	Ventilation method:  louvers at top and bottom of doors

B.	Locker body:  Formed and flanged, with steel stiffener ribs, electric spot welded

C.	Frames:  Formed channel or angle shapes, welded and ground flush, welded to body.

D.	Doors:  Formed steel panel, channel reinforced frame, grind and finish edges

E.	Hinges:  Three butt hinges per door, welded to door and body

F.	Latch:  Recessed, with combination lock

2.5	FINISHES

A.	Clean, degrease and neutralize metal, prime and apply 2 coats of baked enamel.

B.	Paint bodies and doors in contrasting colors.

C.	Door colors to be as selected from manufacturer’s standard colors.

PART 3  EXECUTION

3.1	INSPECTION

A.	Verify that project is ready to receive work of this Section.

B.	[Verify that bases are correctly sized and configured.]

3.2	INSTALLATION

A.	Install according to manufacturer’s installation instructions.

B.	Install lockers plumb and square.

C.	Secure lockers with fasteners appropriate for substrate.

D.	Bolt adjoining locker units together to provide a rigid installation.

E.	Install end panels, filler panels and sloping tops.

F.	Install accessories.

3.3	CLEANING

A.	Clean locker interior and exterior surfaces.

END OF SECTION

*****************************************************************

Do not delete the following reference information:

*****************************************************************

FOR LANL USE ONLY

This project specification is based on LANL Master Specification 10 5113 Rev. 1, dated May 16, 2008.